## Slide 1: A6445 – Major Project Phase - II Domain: VLSI
VARDHAMAN COLLEGE OF ENGINEERING, HYDERABAD
Autonomous institute, affiliated to JNTUH
Enhancing Real-Time Clock with a Low-Power Crystal Oscillator and Pulsed Driver
By
20881A04J6 – B Sathwika
21885A0423 – V Aakash Chandra
20881A04J7 – B Laxminarayana
Under the guidance of
Dr. C. Padmini
Associate Professor, Dept. of ECE
Team No. - 2020040415

## Slide 2
Enhancing Real-Time Clocks with a Low-Power Crystal Oscillator and Pulsed Driver
Outline:
Objectives
Motivation
Introduction
Literature Review
Block Diagram
Circuit Diagram
Execution Flow
References

## Slide 3
The main objective of this project are
  To enhance the performance of Real-Time Clocks (RTCs) by integrating a low-power crystal oscillator and pulsed drivers.
  To replace traditional amplifiers with pulsed drivers, incorporating Delay Locked Loop (DLL) and Switched Capacitor Networks (SCN) for precise pulse generation and programmable time delays.
Objectives:
Enhancing Real-Time Clocks with a Low-Power Crystal Oscillator and Pulsed Driver

## Slide 4
The Real Time Clock’s main motive is to timestamp data, schedule events, manage power and for the data accuracy.
As the demand for energy-efficient and accurate timekeeping continues to rise, there is a pressing need to optimize RTC technology.
By integrating a low-power crystal oscillator and innovative pulsed driver technology, this project seeks to address this challenge.
These enhances the RTC accuracy and stability while also conserving energy and improving overall system performance.
Motivation:
Enhancing Real-Time Clocks with a Low-Power Crystal Oscillator and Pulsed Driver

## Slide 5
A Real-Time Clock (RTC) is a crucial component in electronics that require accurate timekeeping and timestamping.
RTCs are responsible for tracking the current date and time, even when the device is powered off or in a low-power state.
In generating an RTC, the already implemented Crystal Oscillator which consumes 3.24nW of power over the supply voltage of 1-1.8V with precise crystal values is used.
Amplifiers required for RTC generation can be replaced with pulsed drivers.
Switched Capacitor Networks (SCN) can be used to create programmable time delays by controlling the charging and discharging of capacitors in RTC circuitry.
Introduction:
Enhancing Real-Time Clocks with a Low-Power Crystal Oscillator and Pulsed Driver

## Slide 6
Literature Review:
Enhancing Real-Time Clocks with a Low-Power Crystal Oscillator and Pulsed Driver
S.No | Authors | Title | Year and Publication | Research Finding
1. | Dongmin Yoon, Taekwang Jang, Dennis Sylvester, David Blaauw | A 5.58 nW Crystal Oscillator Using Pulsed Driver for Real-Time Clocks | 2016, IEEE JOURNAL OF SOLID-STATE CIRCUITS | A Real-Time Clock generation using pulsed drivers and Low power crystal oscillators In Cadence Virtuoso 180nm CMOS Technology.
2. | Mariana Siniscalchi , Fernando Silveira Carlos Galup-Montoro | Ultra-Low-Voltage CMOS Crystal Oscillator | January 28, 2020. IEEE TRANSACTIONS ON CIRCUITS AND SYSTEMS–I: REGULAR PAPERS | 32KHz Crystal is proposed with specific L and C values. Used 2 different approaches for better oscillator consideration. Used Schmitt Trigger for low power consumption and losses
3 | Dongmin Yoon, Taekwang Jang, Dennis Sylvester, David Blaauw | “A 5.58 nW 32.768 kHz DLL-assisted XO for real-time clocks in wireless sensing applications | Feb. 2012, IEEE Int. Solid-State Circuits Conf. Dig. Tech. Papers (ISSCC), pp. 366–368 | DLL and SCN Networks are introduced with different configuration. Different SCN config. Are taken.

## Slide 7
7
Literature Review:
Enhancing Real-Time Clocks with a Low-Power Crystal Oscillator and Pulsed Driver
S.No | Authors | Title | Year and Publication | Research Finding
4. | Zule Xu , Noritoshi Kimura, Kenichi Okada | Ultralow-Power Class-C Complementary Colpitts Crystal Oscillator | July 21, 2020. IEEE SOLID-STATE CIRCUITS LETTERS, VOL. 3 | Proposed Class C Colpitts Crystal Oscillator using CMOS technology for Low Power applications with 24MHz XO 7-μW steady-state power consumption.
5. | Shunta Iguchi, Takayasu Sakurai, Fellow,Makoto Takamiya, | A Low-Power CMOS Crystal Oscillator Using a Stacked-Amplifier Architecture | 2017 IEEE JOURNAL OF SOLID-STATE CIRCUITS | Low power 39.25MHz XO with 4 stages of stacked amplifiers Used 65nm CMOS Technology
6. | Y. Kim, D. Sylvester, and D. Blaauw | Limited contention level converter for robust wide-range voltage conversion | Jun. 2011, IEEE Symp. VLSI Circuits Dig. Tech. Papers, pp. 188–189. | Level Converters are introduced and varied with different voltage levels. CMOS 180nm Technology

## Slide 8
8
Literature Review:
Enhancing Real-Time Clocks with a Low-Power Crystal Oscillator and Pulsed Driver
S.No | Authors | Title | Year and Publication | Research Finding
7. | S. Lin, D. Sylvester, and D. Blaauw, | A 150 pW program-and-hold timer for ultra-low-power sensor platforms,” | Feb. 2009, IEEE Int. Solid-State Circuits Conf. Dig. Tech. Papers (ISSCC), pp. 326–327 | Timer and Hold Circuits are introduced. CMOS 180nm Technology
8. | . Lim, I. Lee, D. Sylvester, and D. Blaauw, | Batteryless sub-nW cortexM0+ processor with dynamic leakage-suppression logic | Feb. 2015, IEEE Int. Solid-State Circuits Conf. Dig. Tech. Papers (ISSCC), pp. 146– 147. | Dynamic-leakage suppression logic is introduced in the project. CMOS 180nm Technology

## Slide 9
Block Diagram:
Enhancing Real-Time Clocks with a Low-Power Crystal Oscillator and Pulsed Driver
Fig. Block Diagram of Real-Time Clock
Pre Amplifier
Output Driver
NMOS
Crystal Oscillator(3.24nW)
Preamplifier:
Here Preamplifier is kept before the output driver as the small input signal before reaching to output driver must be amplified.
Output Drivers:
By giving the amplified output to the drivers, this results in maximum gate-to-source voltage, minimized ON resistance and giving oscillations with minimum energy loss in the transistor.

## Slide 10
10
10
10
Block Diagram:
Enhancing Real-Time Clocks with a Low-Power Crystal Oscillator and Pulsed Driver
Fig. Block Diagram of Crystal Oscillator with 3.24nW Power Consumption
XO Circuit:
Has low power consumption of 3.24nW
Schmitt Trigger is used in place of Op-Amp that minimizes its limitations.
Bond Wire is used that reduces the power.
32KHz Crystal is used with specific L and C values, for WSN applications where low power and low voltage is required.

## Slide 11
11
Circuit Diagram:
Enhancing Real-Time Clocks with a Low-Power Crystal Oscillator and Pulsed Driver
Fig. Circuit Diagram of Front End Block
FE Block:
Front End block consists of body biased inverter and generator.
It converts sine wave oscillations to the square wave to generate input for next block i.e. DLL.
Body Biased Inverter amplify the sine wave
Body Biased generator dynamically adjusts the body bias, so that trip voltage is set as required.
Fig. Circuit Diagram of DLL(Delay Locked Loop)
DLL Block:
Made with current-starved inverters that minimizes the leakage.
A pair of output from DLL chosen by the MUX for next block i.e. Pulse Generator.

## Slide 12
Fig. Charge Pump Circuit
Fig. Edge detector circuit
12
12
Circuit Diagram:
Enhancing Real-Time Clocks with a Low-Power Crystal Oscillator and Pulsed Driver
Edge Detector and Charge Pump for DLL:
Uses custom cells instead of Flip Flops to reduce number of transistor count.
Only used when it is needed to minimize the overall power consumption (Double stacking is used)
Works periodically

## Slide 13
13
13
Circuit Diagram:
Enhancing Real-Time Clocks with a Low-Power Crystal Oscillator and Pulsed Driver
Fig. Level Converter Circuit
Level Converter:
The medium-voltage supply for pulse generated from previous block is up-converted to the high-voltage supply level for low ON-resistance.
For NMOS driver, converted to high voltage, the maximum voltage is increased to Vddh.
For PMOS driver, the minimum voltage needs to be decreased to Vssh.

## Slide 14
14
14
Circuit Diagram:
Enhancing Real-Time Clocks with a Low-Power Crystal Oscillator and Pulsed Driver
Fig. Block Diagram of Switched Capacitor Network (SCN)
SCN:
Parasitic components are considered for high SCN efficiency which minimizes the effect of higher ripple in supply voltage.
SCN-1 generates the medium-voltage supply from high-voltage supply pair.
SCN-2 generates the low-voltage supply from medium-voltage supply pair.
Triple well was used to reduce the power consumption
Uses an external clock for its operation

## Slide 15
15
15
15
Circuit Implementation:
Enhancing Real-Time Clocks with a Low-Power Crystal Oscillator and Pulsed Driver
Fig. Schematic Diagram of Front End Block in Cadence

## Slide 16
16
16
16
16
Circuit Implementation:
Enhancing Real-Time Clocks with a Low-Power Crystal Oscillator and Pulsed Driver
Fig. Schematic Diagram of Delay Cells in DLL Block in Cadence

## Slide 17
17
17
17
17
17
Circuit Implementation:
Enhancing Real-Time Clocks with a Low-Power Crystal Oscillator and Pulsed Driver
Fig. Schematic Diagram of FE, DLL, MUX
Fig. Schematic Diagram of 2x1 MUX

## Slide 18
18
18
18
18
18
18
Circuit Implementation:
Enhancing Real-Time Clocks with a Low-Power Crystal Oscillator and Pulsed Driver
Fig. Circuit Diagram of SCN-1 conf. B

## Slide 19
19
19
19
19
19
19
Circuit Implementation:
Enhancing Real-Time Clocks with a Low-Power Crystal Oscillator and Pulsed Driver
Fig. Circuit Diagram of SCN-2 conf. B

## Slide 20
20
20
20
20
20
20
Previous Crystal Oscillator Output:
Enhancing Real-Time Clocks with a Low-Power Crystal Oscillator and Pulsed Driver

## Slide 21
21
21
21
21
21
21
21
Expected Output:
Enhancing Real-Time Clocks with a Low-Power Crystal Oscillator and Pulsed Driver
Fig. Expected Waveforms of RTC using XO

## Slide 22
References:
Enhancing Real-Time Clocks with a Low-Power Crystal Oscillator and Pulsed Driver
[1] D. Yoon, T. Jang, D. Sylvester, and D. Blaauw, “A 5.58 nW crystal oscillator using pulsed driver for real-time clocks,” IEEE J. Solid-State Circuits, vol. 51, no. 2, pp. 509–522, Feb. 2016.
[2] Siniscalchi, Mariana, Fernando Silveira, and Carlos Galup-Montoro. "Ultra-low-voltage CMOS crystal oscillators." IEEE Transactions on Circuits and Systems I: Regular Papers 67.6 (2020): 1846-1856. [3] Xu, Zule, et al. "Ultralow-power class-c complementary colpitts crystal oscillator." IEEE Solid-State Circuits Letters 3 (2020): 274-277.[4] Melek, Luiz Alberto Pasini, Márcio Cherem Schneider, and Carlos Galup-Montoro. "Operation of the classical CMOS Schmitt trigger as an ultra-low-voltage amplifier." IEEE Transactions on Circuits and Systems II: Express Briefs 65.9 (2017): 1239-1243.
[5] Iguchi, Shunta, Takayasu Sakurai, and Makoto Takamiya. "A low-power CMOS crystal oscillator using a stacked-amplifier architecture." IEEE Journal of Solid-State Circuits 52.11 (2017): 3006-3017.

## Slide 23
Any Questions/Discussions ???
Enhancing Real-Time Clocks with a Low-Power Crystal Oscillator and Pulsed Driver

## Slide 24
Thank You !!!
Enhancing Real-Time Clocks with a Low-Power Crystal Oscillator and Pulsed Driver